## Slide 1
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
InterfaceHouseKeeping message structure
DataItem1
DataItem2
DataItem3
DataItem4
DataItem5
DataItem6
DataItem7
DataItem8
Legend:
DataItem1: Nominal transceiver circuit voltage (double).
DataItem2: Redundant transceiver circuit voltage (double).
DataItem3: Internal power supply measured with nominal ADC (double).
DataItem4: Internal power supply measured with redundant ADC (double).
DataItem5: Main board PCB temperature measured by sensor 1 (double).
DataItem6: Main board PCB temperature measured by sensor 2 (double).
DataItem7: Sun sensor board PCB temperature from sensor 3 (double).
DataItem8: Sun sensor board PCB temperature from sensor 4 (double).
0
1
2
3
InterfaceStatus message structure
Data Item1
Legend:
DataItem1: Bit 0 to 2, provide information about last reset. Bit 3 indicates if ADCS is ready. Bit 4 indicates if there is an OBC communication error. Bit 5 indicates if there is a communication error with one of the units controlled by the ADCS (binary).
DataItem2: Each bit indicates the unit in error (Gyroscope, Reaction Wheel, Magnetorqer, Magnetometer, Sun Sensor) (binary).
DataItem3: Watchdog reset counter value incremented at every watchdog reset (integer).
DataItem4: Overall reset counter value incremented at every device reset (integer).
Data Item2
Data Item3
Data Item4
Magnetorquer Set PWM RSP message structure
Legend:
DataItem1: Unit identifier, nominal or redundant (binary).
DataItem2: Magnetorqer nX current (double).
DataItem3: Magnetorqer nY current (double).
DataItem4: Magnetorqer nZ current (double).
0
1
2
3
4
5
6
Data Item1
DataItem2
DataItem3
DataItem4